## Slide 1: Chapter 12 – Water: Removing Dissolved Solutes
Week 2, Lesson 1

## Slide 2: Precipitation Reactions
When two solutions are mixed, an insoluble compound sometimes forms; that is, a solid forms and separates from the solution.
This solid is called a precipitate.

## Slide 3: Precipitation Example
Barium chloride is a soluble compound containing barium ions and chloride ions.
Sodium sulfate is also a soluble compound and contains sodium ions and sulfate ions.
When solutions of barium chloride and sodium sulfate are added together, the mixture is initially supersaturated with barium sulfate.
A white precipitate, barium sulfate, forms.
This reaction is represented by the equation:
BaCl2(aq) + Na2SO4(aq)  BaSO4(s) + 2NaCl (aq)

## Slide 4: Precipitation Example cont…
The precipitate of barium sulfate can be collected by filtering the solution.
If the water is evaporated from the filtrate (the remaining solution), solid sodium chloride remains.
You can use the solubility guide to identify which products in a precipitation reaction will be the solid, or precipitate.

## Slide 5: Worked Example
A precipitate forms when a colourless solution of lead nitrate (Pb(NO3)2) is added to a colourless solution of potassium iodide (KI). A dense yellow colour appears that is solid lead iodide. Write a balanced chemical equation, identifying the precipitate.
STEP 1: Identify the possible products of the reaction by swapping the positive and negative ions of the reactants.
STEP 2: Write the correct formulas for the reactants and possible products.
STEP 3: Write the equation and balance it so that equal numbers of all atoms occur on both sides.
STEP 4: Deduce from the solubility table, which of the products will precipitate. This is given the symbol (s) while the soluble reactants and products are given the symbol (aq).

## Slide 6: Ionic Equations
In the reaction between the solutions of barium chloride and sodium sulfate, the equation is often written:
BaCl2(aq) + Na2SO4(aq)  BaSO4(s) + 2NaCl (aq)
However, when ionic substance dissolve in water, the ionic compounds dissociate into their ions in solution. This means that it is free ions that are reacting to form a precipitate and the equation is more accurately expressed as:
Ba2+(aq) + 2Cl-(aq) + 2Na+(aq) + SO42-(aq) BaSO4(s) + 2Na+(aq) + 2Cl-(aq)

## Slide 7: Ionic Equations cont…
Barium sulfate, being insoluble, in not dissociated into ions.
It precipitates and so is written as a compound in solid state.
All others are soluble and are written as ions.
Looking at the reaction, it can be seen that the only change that occurs is that barium ions and sulfate ions have combined.
The sodium and chloride ions have not reacted, they have remained as ions in the same state at the end of the reaction.
Ions such as these are called spectator ions and may be taken out of the equation.
So the reaction can be represented by:
Ba2+(aq) + SO42-(aq)  BaSO4(s)

## Slide 8: Ionic Equations cont…
This type of equation is called an ionic equation.
Ionic equations are simpler than full equations and focus on the actual reaction taking place.
Sometimes, however, a full equations is preferred so you can tell which particular compound will dissolve in water to provide a source of an ion.

## Slide 9: Maintaining Water Quality
Water’s ability to dissolve a wide range of materials causes problems when unwanted or toxic solutes pollute water supplies.
Water often needs to be treated before it is consumed.
Some waste water also needs to be treated before being returned to the environment.
Precipitation reactions play an important role in the treatment of drinking water.
Week 2, Lesson 2

## Slide 10: Treatment of Drinking Water
In most Australian cities water is treated before being passed on to consumers through the water supply system.
The amount of treatment required varies from city to city, but the usual purpose is to remove suspended solids, bacteria, colour and odour.
The steps involved in the purification of water are:
  Flocculation
  Settling of the ‘floc’
  Filtering
  Chlorination

## Slide 11: Treatment of Drinking Water
A typical system used for treatment of water…

## Slide 12: Flocculation
Is the process by which small suspended particles in the water join together to form larger heavier particles.
The heavier particles then sink and settle in the water sample.
Flocculation can be achieved by adding alum (aluminium sulfate) and if necessary, lime (Ca(OH)2).
Lime is added to neutralise acides and provide a source of hydroxide ions on the water supply.
Lime is an ionic compound which dissolves in the water and dissociates into its ions.

## Slide 13: Flocculation cont…
Alum provides Al3+ ions in solution and these combine with hydroxide ions to form a precipitate of aluminium hydroxide.
Aluminium hydroxide is produced in the form of a gelatinous precipitate called the floc.
This traps other fine particles and removes colour and some microorganisms from the water.

## Slide 14: Flocculation

## Slide 15: Settling
The water is left to stand to allow the floc to settle for a period.
During this time, the settled materials form a sludge.
The rest of the water passes on to the filtering stage.
The sludge accumulates at the bottom of the settling tank and is removed.

## Slide 16: Settling

## Slide 17: Filtering
Water from the settling tank is allowed to filter down through a bed of sand over gravel. This removes any remaining suspended matter.

## Slide 18: Filtering

## Slide 19: Chlorination
The clear water is usually treated with gaseous chlorine to destroy bacteria.
The main purpose of chlorination is to remove biological contaminants.
It is the hypochlorous acid (HOCl) that kills the bacteria.
HOCl diffuses through the cell walls of the microorganisms and destroys their ability to function.
After chlorination water is considered fit for human consumption.

## Slide 20: Chlorination

## Slide 21: Hard Water
Melbourne has a supply of soft water.
This means that it is easy to produce a lather of soap.
Some areas of Australia produce hard water, which means more soap has to be used to produce a lather.
As well as problems caused with soaps, hard water causes deposits to form on the inside of kettles or water pipes.
These deposits can lead to blocking of pipes.
Hardness in water is caused by the presence of some metal ions, mainly calcium, magnesium and iron.
These metals interfere with the washing action of soap and detergents.

## Slide 22: Hard Water cont…
One of the essential ingredients in soap is the compound sodium stearate (C17H35COO-Na+).
In water this produces stearate ions which act as the dirt remover.
The metal ions in hard water combine with this ion to produce a precipitate, so it removes the stearate ions from the solution.

## Slide 23: Desalination
Sea water contains about 3.5% dissolved salts and so is not suitable for drinking or agriculture.
Desalination involves the removal of salts from sea water to obtain fresh water.
There are a number of methods used to desalinate water.

## Slide 24: Distillation
Is an effective way of removing water from salts.
If a salt solution is boiled in apparatus the water vapour will pass over into a condenser , leaving the non-volatile ions in the original flask.
The water vapour is then cooled and liquefied in the condenser and recovered.
In this way the water and the dissolved salts are separated from each other.
Distillation is relatively expensive to carry out, however, is usually not used on a large scale.

## Slide 25: Reverse Osmosis
Osmosis is the natural tendency of water to move from a region of low salt concentration to one of higher salt concentration.
If salt water and fresh water are separated by a semi permeable membrane that allows water molecules through, but not dissolved ions to pass, the water molecules will spontaneously pass through the membrane from fresh water to salt water.
This can be reversed if pressure is applied to the salt water side.
This process is known as reverse osmosis.
The difficulty and associated cost of this process is in making suitable membrane that will not rupture under the high pressure used.

## Slide 26: Reverse Osmosis cont…

## Slide 27: Ion Exchange
Another effective method of removing dissolved salts from seawater is ion exchange.
A ion-exchange resin is a very large polymetric molecule with many charge sites along the polymer.
This resin is packed into a cylinder and salt water is allowed to pass slowly through.
Both cation and anion exchange resins are used.

## Slide 28: Ion Exchange cont…
As the salt water first travels through a cation-exchange resin, Na+(aq) ions become attached to the negative groups on the resin, displacing H+(aq) ions from the resin into the water.
Therefore being an exchange of cations on the resin.
The water then flows through a second cylinder containing anion-exchanged resin which will exchange anions such as Cl- and SO42- for OH- ions.
These OH- ions combine with the H+ ions for produce water.
Water treated in this way contains virtually no ions and is said to be deionised.
Many school labs use this deionised water instead of distilled water.
The process produces high quality drinking water but is expensive.