## Slide 1: Chapter 8 – Mass Spectrometry

## Slide 2: Mass Spectrometry
The mass spectrometer can be used for:
  Quantitative analysis – as a sophisticated and very sensitive detector that can measure how much of a substance is present.
  Qualitative analysis – to provide a unique fingerprint of a substance; this can be used to identify the substance from an online database or to give information about the structure of a new or unknown compound.

## Slide 3: Instrumentation
The key principle of mass spectrometry is that a charged particle passing through a magnetic field is deflected along a circular path of radius proportional to the mass-to-charge ratio, m/e.

## Slide 4: Instrumentation cont…
The sample as a gas, enters the evaluated tube.
Positive ions are formed in the ionisation chamber when an electron beam dislodges electrons from the sample atoms or molecules.
The positive ions are accelerated by an electric field.
The ions enter a magnetic field perpendicular to their path. This cause the ions to move in a curved path with a radius that depends upon the mass-to-charge ratio of the ions.
Only ions moving in a curved path of a particular radius, corresponding to a fixed m/e ratio, will reach the collector.
Particles of different m/e ratio are able to reach the collector through adjustments to the accelerating voltage or the strength of the magnetic field.
The collector measure the current due to the ions reaching the detector and the data is recorded as a mass spectrum.

## Slide 5: How the Spectrum is formed
A molecular substance can give a range of peaks in the spectrum.
Two factors can cause the many peaks in the spectrum:
  The fragmentation of the molecules into a large number of different positive ions.
  The occurrence of different isotopes of the atoms that make the molecules.

## Slide 6: Fragmentation
The high energy electron beam can knock just one electron from the molecule, M, to form a positive ion.
M+ is called the molecular ion or parent molecular ion.
The parent molecular ion is a radical, with one unpaired electron.
It is chemically unstable and so will often break into smaller fragments consisting of more positive ions and uncharged free radicals.

## Slide 7: Fragmentation example…
Ethanoic acid will ionise as follows:
CH3COOH + e-  CH3COOH+ + 2e-
parent molecular ion; m/e = 60
CH3COOH+ will fragment:
CH3COOH+  CH3+ + COOH
fragment ion m/e = 15 uncharged free radical
The CH3+ may fragment further:
CH3+  CH2+ + H
fragment ion m/e = 14

## Slide 8: Fragmentation cont…
When an ion fragments into two smaller parts, one ion will retain the electron to become the uncharged free radical and the other is positively charged.
There are always two possibilities: either fragment could theoretically become the charged ion.
The molecular ion can break into almost every type of fragment, down to individual atom.
Only the positive ions reach the detector.
The uncharged radicals are evacuated by the vacuum pump.

## Slide 9: Isotope Effects
In the same spectrum, additional peaks can be formed due to the occurrence of different isotopes of an element.
For example chlorine has two isotopes, Cl35 and Cl37.
As a result, the mass spectrum of CH3Cl shows a peak at m/e = 50 and m/e = 52.
There are two molecular ions, one due to the molecule with 35Cl and the other to the molecule with 37Cl.

## Slide 10: Interpreting Mass Spectra
The height of the peak in the mass spectrum gives the relative concentration of the ions present.
The highest peak, the base peak, is given an intensity of 100%.
The intensities of all other peaks are measured relative to the base peak.

## Slide 11: Interpreting Mass Spectra cont…
The relative intensities of the ions depend on:
  The energy of the bombarding electrons
  The stability of the ion fragments formed
  The ease with which ions can lose atoms
The peaks with the greatest mass will often give the relative molecular mass of the molecule.
However, in many cases the peak from the parent molecular ion may be so weak as to be unnoticeable.
The difference in mass between the fragment ions can give information about the structure of the molecule.

## Slide 12
The mass spec of ethanoic acid, shows that the parent molecular ion has a mass of 60.
The fragment corresponding to the peak mass at 45 is 15 units lighter than the parent molecular ion, indicating that the CH3COOH+ has lost a CH3 group to form the COOH+ fragment, which has a mass of 45.

## Slide 13: Uses of Mass Spec
Mass spec can be used to analyse many organic molecules.
Applications include the analysis of pharmaceutical samples, environmental samples; such as contaminant in water and geological samples; such as oil and gas, and medical screening.

## Slide 14: Combined Techniques
The most commonly used combined techniques are gas chromatography-mass spectrometry and high performance liquid chromatography-mass spectrometry.

## Slide 15: Chromatography & Mass Spec
The advantage of Chromatography and Mass Spectrometry is that the chromatography can separate a complex sample into any number of components and each one can be positively identified through mass spec.

## Slide 16: Synchrotron
A synchrotron is a giant collection of spectrometers linked via circular channels and covering an area equal to half a football field.
A synchrotron accelerate and circulates electrons to close to the speed of light.
The electrons are accelerated by magnets in a linear accelerator and in a booster ring and then transferred to an outer storage ring.
As the electrons’ paths are bent through magnetic fields, the electrons generate electromagnetic radiation across the spectrum from infrared to X-ray.
The radiation is channelled down ‘beam lines’ where it is used as the source radiation for a range of chemical instruments.

## Slide 17: Synchrotron cont…
Synchrotrons have a number of advantages over conventional spectrometers:
  The electromagnetic radiation is hundreds of thousands of times more intense.
  A wide energy spectrum from infrared to X-rays is produced.
  The radiation can be very finely tuned to select precise frequencies
  The radiation is highly polarised
  Short intense pulses of radiation lasting less than a nanosecond are produced.

## Slide 18
Read combining analyses to learn more: Analysis of Ethanol in own time.

## Slide 19: Assessing Analytical Techniques
Factors to consider when choosing an analytical technique fall into two categories: chemical considerations and economic factors.

## Slide 20: Chemical Considerations
Analyte: consider whether the analyte used is non-metal or metal. Is it coloured or transparent? Is it volatile? Soluble?
Sample: Consider the amount of sample available, the concentration of the analyte in the sample, the physical state of the sample and possible interference from other compounds in the sample.

## Slide 21: Economic Considerations
Time: the time taken depends on whether a single analysis is to be performed per day or if hundreds of samples are to be analysed per day, and if continuous monitoring, multi-element determination, or complex sample preparation are needed.
Cost of equipment
Expertise
Quality data: costs are generally greater for high quality data.